## Slide 1: NCCloud: Applying Network Coding for the Storage Repair in a Cloud-of-Clouds
Yuchong Hu1, Henry C. H. Chen1, Patrick P. C. Lee1, Yang Tang2
1The Chinese University of Hong Kong 2Columbia University
FAST’12

## Slide 2: Cloud Storage
Cloud storage is an emerging service model for remote backup and data synchronization
Single-cloud storage raises concerns:
  Cloud outage
  Vendor lock-ins [Abu-Libdeh et al., SOCC’10]
    Costly to switch cloud providers

## Slide 3: Multiple-Cloud Storage
Solution: multiple-cloud storage
  Deploy a proxy between users and multiple clouds
  Stripe data across multiple clouds
(n,k) MDS code: Any k out of n storage nodes (clouds) can rebuild original file.
e.g., RAID-5: k = n – 1; RAID-6: k = n – 2
Proxy
Cloud 1
Cloud 2
Cloud 3
Cloud 4
Users
file
upload
download
file

## Slide 4: Repairing a Failed Cloud
How to repair:
Proxy
Cloud 1
Cloud 2
Cloud 3
Cloud 4
Cloud 5
Repair traffic =
＋
＋
Goal: minimize repair traffic
  Repair traffic: amount of data read from surviving clouds
  Hence minimize monetary cost due to data migration

## Slide 5: Reed Solomon Codes
Conventional repair:
  Repair whole file and reconstruct data in new node
A
B
A+B
A+2B
B
A+B
A
A
A
B
File of
size M
Node 1
Node 2
Node 3
Node 4
Proxy
Reed Solomon codes
Repair traffic = M
n = 4, k = 2

## Slide 6: Regenerating Codes
Repair in regenerating codes:
  Downloads one chunk from each node (instead of whole file)
  Repair traffic: save 25% for (n=4,k=2), while same storage size
  Using network coding: encode chunks in storage nodes
A
B
C
D
A+C
B+D
A+D
B+C+D
C
A+C
A+B+C
A
B
A
B
C
D
A
B
Node 1
Node 2
Node 3
Node 4
File of
size M
Proxy
Regenerating codes
Repair traffic = 0.75M
n = 4, k = 2
[Dimakis et al.’10]

## Slide 7: Related Work
Theoretical analysis
  Regenerating codes [Dimakis et al. ’10] exploit the optimal trade-off between storage and repair traffic.
Empirical studies
  e.g., [Gkantsidis & Rodriguez ’05], [Dunimuco & Biersack ’09], [Martalo et al. ’11]
    Evaluate random linear codes
    Based on simulations
Multiple cloud storage
  e.g., HAIL [Bowers et al. ’09], RACS [Abu-Libdeh et al. ’10], DEPSKY [Bessani et al. ’11]
  Based on erasure codes

## Slide 8: Challenges
Implementation of regenerating codes in multiple cloud storage:
  Can we eliminate encoding/decoding operations in storage nodes (clouds)?
    Only standard read/write interfaces would suffice
  Can we support basic upload/download operations with regenerating codes?
  Can we support the repair function with regenerating codes?

## Slide 9: Our Work
Build NCCloud, a proxy-based storage system that applies regenerating codes in multiple-cloud storage
Design goals:
  Propose an implementable design of functional minimum-storage regenerating (F-MSR) code
  Support basic read/write operations and the repair function
  Preserve storage overhead as in MDS codes, while reducing repair traffic
Implement and evaluate NCCloud in real storage setting
  focus on double-fault tolerance (k = n-2)
  focus on single-fault recovery
  built on FUSE

## Slide 10: F-MSR: Key Idea
Code chunk Pi = linear combination of original data chunks
Repair in F-MSR:
  Download one code chunk from each surviving node
  Reconstruct new code chunks (via random linear combination) in new node
P1
P2
P3
P4
P5
P6
P7
P8
P3
P5
P7
P1’
P2’
A
B
C
D
P1’
P2’
Node 1
Node 2
Node 3
Node 4
File of
size M
Proxy
n = 4, k = 2
F-MSR codes
Repair traffic = 0.75M

## Slide 11: F-MSR: Key Idea
F-MSR: non-systematic
  Doesn’t keep original data as in systematic codes
  Stores only linearly combined code chunks
    while maintaining MDS property
  Suitable for rarely-read long-term archival
With (non-systematic) F-MSR,
  Eliminate need of encoding/decoding in clouds
  Keep the benefits of network codes in storage repair
  For k = n-2 (double-fault tolerance)
    n = 4: repair traffic saved by 25%
    For very large n: repair traffic saved by almost 50%

## Slide 12: NCCloud: Upload
Encoding process:
  Pi = ECVi × [A,B,C,D]T
    ECVi : encoding coefficient vector of Pi
    Arithmetic operations in GF(28)
  EM = [ECV1,ECV2,…,ECVn]T
    EM: encoding matrix is replicated to all nodes as metadata
P1
P2
P3
P4
P5
P6
P7
P8
A
B
C
D
k(n-k) chunks
Proxy
divide
encode
P1
P2
P3
P4
P5
P6
P7
P8
n(n-k) chunks
distribute
File
n=4, k=2
Storage nodes

## Slide 13: NCCloud: Download
Decoding process:
  [A,B,C,D]T = EM -1× [P1,P2, P3, P4]T
    Download all the chunks from any k of n clouds
    Multiply inverted encoding matrix with downloaded chunks
P1
P2
P3
P4
P5
P6
P7
P8
A
B
C
D
k(n-k) chunks
Proxy
merge
decode
P1
P2
P3
P4
k(n-k) chunks
download
File
n=4, k=2
Storage nodes

## Slide 14: NCCloud: Iterative Repair
Repair: generate random linear combinations of chunks
How to keep iterative single-failure repairs sustainable?
  i.e., how to ensure new code chunks don’t break MDS property?
Solution: two-phase checking
  MDS property check
    Current repair maintains MDS property
  Repair MDS property check
    Next repair for any possible failure maintains MDS property
Simulations show the importance of two-phase checking over MDS property check only
  See paper for details

## Slide 15: NCCloud: Iterative Repair
P1
P2
P3
P4
P5
P6
P7
P8
Proxy
×
Get all the existing ECVs:
ECV3, ECV4, ECV5, ECV6, ECV7, ECV8
Randomly select one ECV from each existing nodes:
ECV3, ECV5, ECV7
Randomly generate a repair matrix: RM
Obtain ECVs in new node:
[ECV’1, ECV’2]= RM × (ECV3, ECV5, ECV7)T
Construct a new EM’ and test it:
EM’ = [ECV’1, ECV’2, ECV3, ECV4, ECV5, ECV6, ECV7, ECV8]
Check both MDS and repair MDS property in EM’.
fail
Download P3,P5,P7; regenerate (P1’,P2’)= RM × (P3, P5, P7)T
P1’
P2’
Storage nodes
n=4, k=2

## Slide 16: Cost Analysis
Repair traffic cost
  F-MSR saves 25% (for n = 4) compared to conventional repair
Metadata of F-MSR
  Metadata size = 160B; file size = several MBs
Overhead due to GET requests during repair
  Assuming S3 plan in Sep 2011, n = 4, k = 2, file size = 4MB
  Conventional repair: 0.427%
  F-MSR repair: 0.854%
Monthly price plan as of Sep 2011

## Slide 17: Experiments
NCCloud deployment
  Single machine connected to a cloud-of-clouds
  n = 4, k = 2
Coding schemes
  Reed-Solomon-based RAID-6 vs. F-MSR
Metric
  Response time
Cloud environments:
  Local cloud: OpenStack Swift
  Commercial cloud: multiple containers in Azure

## Slide 18: Response time: Local Cloud
F-MSR has higher response time due to encoding/decoding overhead
F-MSR has slightly less response time in repair, due to less data download
Chart: 
| 1 | 10 | 50 | 100 | 200 | 300 | 400 | 500
RAID-6 | 0.557 | 1.288 | 4.9532 | 9.262 | 17.4028 | 25.7437 | 34.0742 | 43.0275
F-MSR | 0.56375 | 1.3853 | 5.3297 | 9.7447 | 18.9228 | 27.6177 | 36.536 | 45.4457
File size (MB)
Response time (s)
UPLOAD
File size (MB)
Response time (s)
DOWNLOAD
File size (MB)
Response time (s)
REPAIR
Chart: 
| 1 | 10 | 50 | 100 | 200 | 300 | 400 | 500
RAID-6 | 0.3025 | 0.499 | 1.1718 | 2.0595 | 3.6643 | 4.9465 | 7.165 | 8.2577
F-MSR | 0.3825 | 0.7135 | 1.7568 | 2.8813 | 4.8195 | 6.7385 | 8.9467 | 10.813
Chart: 
| 1 | 10 | 50 | 100 | 200 | 300 | 400 | 500
RAID-6(native) | 1.6558 | 2.3585 | 4.9925 | 8.5245 | 14.4447 | 20.5707 | 27.6192 | 33.0502
RAID-6(parity) | 1.6307 | 2.1942 | 5.1223 | 8.5237 | 14.6855 | 20.5318 | 27.674 | 33.2547
F-MSR | 1.701 | 2.298 | 5.1285 | 8.3185 | 14.4497 | 20.2315 | 25.5665 | 31.7722

## Slide 19: Response time: Commercial Cloud
No distinct response time difference, as network fluctuations play a bigger role in actual response time
File size (MB)
Response time (s)
UPLOAD
File size (MB)
Response time (s)
DOWNLOAD
Response time (s)
REPAIR
File size (MB)
Chart: 
| 1 | 2 | 5 | 10
RAID-6 | 1.1182 | 1.5305 | 2.8822 | 4.713
F-MSR | 1.1265 | 1.5928 | 2.8715 | 4.962
Chart: 
| 1 | 2 | 5 | 10
RAID-6 | 0.74625 | 0.934 | 1.4152 | 2.1393
F-MSR | 0.80625 | 0.97825 | 1.5325 | 2.2395
Chart: 
| 1 | 2 | 5 | 10
RAID-6(native) | 3.3015 | 3.467 | 4.369 | 5.4553
RAID-6(parity) | 3.332 | 3.485 | 4.4203 | 5.4577
F-MSR | 3.3472 | 3.511 | 4.2835 | 5.3945

## Slide 20: Conclusions
Propose an implementable design of F-MSR:
  Preserve storage cost, but use less repair traffic
Build NCCloud, which realizes F-MSR
Source code:
  http://ansrlab.cse.cuhk.edu.hk/software/nccloud/