## Slide 1: Data Fusion in Sensor Networks

## Slide 2: Outline
Part 1: Introduction
  Background
  Key concepts
Part 2: State-of-the-art Example
  With compressed sensing
  Data gathering in wireless sensor network

## Slide 3: Data Fusion in 3DLBS Framework
Sensor Network
Data Fusion
Spatial Database
Data Mining/Machine Learning

## Slide 4: Introduction
A sensor network comprises of sensor nodes and a base station.
Each sensor node is battery powered and equipped with:
  Integrated sensors
  Data processing capabilities
  Short-range radio communications
Due to their limited power and shorter communication range, sensor nodes perform in-network data fusion.

## Slide 5: Data Fusion Process
A data fusion node collects the results from multiple nodes.
It fuses the results with its own based on a decision criterion.
Sends the fused data to another node/base station.
Advantages:
  Reduces the traffic load.
  Conserves energy of the sensors.

## Slide 6: Challenges (1)
Data from sensor are not perfect
Incompleteness
  Data not collected by design
  Data not collected due to non-response
Sampling Error
  Simple
  Weight Effects
  Clustering

## Slide 7: Challenges (2)
Measurement Error
  Recall Error
  Respond compliance
  Data entry
Model Error
  Imputation
  Weighting error

## Slide 8: Key Concepts in Data Fusion
Three questions needs to be addressed:
First, at what instance does a node report a sensed event?
Second, how does a node fuse multiple reports into a single one?
Third, what data fusion architecture to use?

## Slide 9: Reporting
Periodical reporting: Sensor nodes periodically send reports to the base station.
Base station inquiry response reports: the BS queries sensors in specific regions for current sensed information.
Event triggered reports: The occurrence of a certain event can trigger reports from sensors in that particular region.

## Slide 10: Fusion Detection
Voting: the oldest and most widely used fusion decision method.
Fusion node arrives at a consensus by a voting scheme like:
  Majority voting
  Complete Agreement
  Weighted voting
The popularity of voting arises from its simplicity and accuracy.
Other fusion decision algorithms include probability-based Bayesian Model and stack generalization.

## Slide 11: Fusion Architecture
Centralized:
  Simplest
  A central processor fuses the reports collected by all other sensing nodes.
  Advantage: Erroneous report(s) can be easily detected.
  Disadvantage: inflexible to sensor changes and the workload is concentrated at a single point.

## Slide 12: Fusion Architecture (2)
Decentralized :
  Data fusion occurs locally at each node on the basis of local observations and the information obtained from neighboring nodes.
  No central processor node.
  Advantages:
    scalable and tolerant to the addition or loss of sensing nodes or dynamic changes in the network.

## Slide 13: Fusion Architecture (3)
Hierarchical:
  Nodes are partitioned into hierarchical levels.
  The sensing nodes are at level 0 and the BS at the highest level.
  Reports move from the lower levels to higher ones.
  Advantage:
    Workload is balanced among nodes

## Slide 14: Example Application
Gathering data from wireless sensor network
  No data cleaning
Compressive sensing
Hybrid architecture