## Slide 1: Everlasting Security in Wireless Communications Networks
Dennis Goeckel
University of Massachusetts Amherst
This work is supported by the National Science Foundation under Grants CNS-1019464, CCF-1249275, and ECCS-1309573.
The Chinese University of Hong Kong
August 27,2014

## Slide 2: Motivation
Everlasting Secrecy:
We are interested in keeping something secret forever. A challenge of cryptography (e.g. the VENONA project) is that recorded messages can be deciphered later:
If the primitive is shown not to be hard.
If significant computational advances are made
If the cryptographic scheme is broken.
Information-theoretic secrecy

## Slide 3: Information-theoretic secrecy [Shannon, 1949]
Information is encoded in such a way that Eve gets no information about the message…if the scenario is right
Advantages:
No computational assumptions on Eve.
If the transmission is securely made, it is secure forever.

## Slide 4: Shannon and the one-time pad [C. Shannon, 1949]
Consider perfect secrecy over a noiseless wireline channel:
Desire I(M,gK(M))=0
Questions:
How long must K be for an N-bit message M?
How do you choose gK(M)?
Alice
Bob
Eve
M
gK(M)
Pre-shared key K
?
M
Notes: Alice sends XOR of the message and the Key=> Bob is unable to decode the message because does not have the key.
Highlighted Statement Shannon show you need key as long as message which is an unfulfilling result

## Slide 5: Shannon and the one-time pad [C. Shannon, 1948]
Answers:
You need an N-bit key K for an N-bit message M.
gK(M) = M K
Alice
Bob
Eve
M
M K
Pre-shared key K
?
(M K) K = M
Blah.

## Slide 6: The Alice-Bob-Eve Scenario in Wireless
Alice
Bob
Eve
Building
But the channels might be noisy…it might be Eve in the parking lot
listening…
…in which case Eve’s channel is worse than Bob’s. Can this help get
information-theoretic secrecy?

## Slide 7: The Wiretap Channel [Wyner, 1975; Cheong and Hellman, 1978]
RAB: Capacity of channel from Alice to Bob
RAE: Capacity of channel from Alice to Eve
RAB > RAE
Alice
Bob
Eve
Building
R = log2(1 + SNRAB) – log2(1 + SNRAE)
Gaussian channels:
Positive rate “if Bob’s channel is better”, and Eve gets nothing.
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 8: The Alice-Bob-Eve Scenario in Wireless
Alice
Bob
Eve
Building
But it might not be Eve in the parking lot listening, rather…
…it might be Eve in the building!
Important Challenge: the “near Eve” problem…

## Slide 9: The Alice-Bob-Eve Scenario in Wireless
Alice
Bob
Building
…and you very likely will not know where she is.
Many would argue that we have traded a long-term computational risk (cryptography) for a short-term scenario (information-theoretic secrecy) risk…no thank you!
Eve

## Slide 10: Outline
Information Theoretic security basics
Potential Physical-Layer Solutions
(with Azadeh Sheikholeslami, Hossein Pishro-Nik)
3. Exploiting the Network
(with Sudarshan Vasudevan, Cagatay Capar, Don Towsley)
4. Current and Future Challenges

## Slide 11: Outline
Information Theoretic security basics
Potential Physical-Layer Solutions
(with Azadeh Sheikholeslami, Hossein Pishro-Nik)
3. Exploiting the Network
(with Sudarshan Vasudevan, Cagatay Capar, Don Towsley)
4. Current and Future Challenges
Recall Goal: Keep Eve from recording a signal from which she can later extract the information.

## Slide 12: Outline
Information Theoretic security basics
Potential Physical-Layer Solutions
(with Azadeh Sheikholeslami, Hossein Pishro-Nik)
3. Exploiting the Network
(with Sudarshan Vasudevan, Cagatay Capar, Don Towsley)
4. Current and Future Challenges
Recall Goal: Keep Eve from recording a signal from which she can later extract the information.

## Slide 13: Attacking the Hardware I: Bounded Memory Model
Cachin and Maurer introduced the “bounded memory model” to achieve everlasting secrecy [Cauchin and Maurer, 1997]. An eavesdropper with memory < M cannot store enough to eventually break the cipher.
4/12
[From “blog.dshr.org”]
  1. The density of memories grows quickly (Moore’s Law)
However, it is hard to pick a memory size that Eve cannot use beyond:
2. Memories can be stacked arbitrarily subject only to (very large) space limitations.
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 14: Bounded Conversion Model
1. In the combative sender-eavesdropper game, front-end dynamic range
is a critical aspect of the receiver.
2. A/D Technology progresses very slowly.
3. High-end A/D’s are already stacked to the limit of the jitter.
Perhaps Cachin and Maurer attacked the wrong part of the receiver:
Idea:
Alice
Bob
Eve
1. IT security requires a channel advantage.
Establish cryptographic security
(e.g. Diffie-Hellman)
Use a short-term cryptographic
to establish the channel advantage.
Analog
“Front-End”
A/D
Digital
“Back-End”
Eve’s Receiver
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 15: System model and approach:
5/12
Alice and Bob pre-share an “emphemeral” cryptographic key k to
choose g(.). Note: Key will be handed to Eve after transmission.
k
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 16: System model and approach:
5/12
Alice and Bob pre-share an “emphemeral” cryptographic key k to
choose g(.). Note: Key will be handed to Eve after transmission.
A/D is a non-linear element. Non-commutativity of non-linear
elements: potential information-theoretic security.
k
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 17: System model and approach:
5/12
Alice and Bob pre-share an “emphemeral” cryptographic key k to
choose g(.). Note: Key will be handed to Eve after transmission.
A/D is a non-linear element. Non-commutativity of non-linear elements:
potential information-theoretic security.
k
Secrecy rate is a shaping gain: Rs=Eg[h(X) – h(g(X))]
h(X): differential entropy
…but, unlike traditional “shaping gains”, gain can be huge.
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 18
6/12
Example: Rapid power modulation for secrecy:
Idea: Key used to rapidly power modulate transmitter. Bob’s receiver gain
control can follow, while Eve’s struggles.
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 19
6/12
Rapid power modulation for secrecy:
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 20
6/12
Rapid power modulation for secrecy:
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 21
6/12
Rapid power modulation for secrecy:
Bob’s gain control is correct: input well-matched to A/D span.
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 22
7/12
Rapid power modulation for secrecy:
2. It is easy to show that the optimal strategy (for Eve) is to
pick a single gain G.
Alice sets her parameters to maximize Rs, whereas Eve tries to find
a gain G that minimizes the secrecy rate Rs given Alice’s choice:
Rs=maxS minG Rs(S, G)
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 23
Large gain
Effect of A/D on the signal:
Clipping (due to overflow)
8/12
Rapid power modulation for secrecy:
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 24
Small gain
Effect of A/D on the signal:
Clipping (due to overflow)
Quantization noise (uniformly distributed)
8/12
Rapid power modulation for secrecy:
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 25
Effect of A/D on the signal:
Clipping (due to overflow)
Quantization noise (uniformly distributed)
Trade-off between choosing a large gain and a small gain:
Eve needs to compromise between more A/D overflows or less resolution.
8/12
Rapid power modulation for secrecy:
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 26
(a) Public Discussion
(b) Power modulation
(Although they are not really competing techniques. Power modulation
approach could be used under public discussion.)
What if Eve picks up the transmitter?
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 27
Secrecy rate vs. SNR at Bob, Eve has perfect access to the signal
10/12
Noisy channel to Bob, noiseless channel to Eve.
Alice
Bob
Eve
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 28
Other approaches:
Artificial intersymbol interference (ISI) [ISIT 2013]: Introduce intentional ISI at the transmitter, key gives Bob an advantage in equalization.
Artificial jamming [Asilomar 2014]: Key is used to add a jamming signal, which Bob can pre-cancel at the receiver – unlike seemingly similar approaches in literature, cryptographic key is handed to Eve after transmission.
IT Security Basics PHY-layer Solutions Using the Network Challenges
Needs some jamming
to confuse Eve
Need some signal
power for Bob

## Slide 29
IT Security Basics PHY-layer Solutions Using the Network Challenges
Challenges for Everlasting Secrecy (Alice-Bob-Eve):
Cryptography: Computational assumptions on eavesdropper.
Information-theoretic security: Scenario assumptions on eavesdropper.
Our approach: Assumptions on current conversion capabilities of
eavesdropper.

## Slide 30: Outline
1. Information Theoretic security basics
2. Potential Physical-Layer Solutions
3. Exploiting the Network
4. Current and Future Challenges

## Slide 31
How much secret info can be shared by a network of wireless nodes in the presence of eavesdropper nodes? [Gupta/Kumar et al]
The Network Scale:
Alice
Bob
Eve
So far we have considered (perhaps not so successfully):
But perhaps we should consider:
… and how many
eavesdroppers
can the network tolerate?
Questions:
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 32
Gupta-Kumar: n nodes each can share bits per second.
Want to achieve this throughput securely, in the presence of m eavesdroppers of unknown location.
n good guys (matched into pairs)
m bad guys.
Problem: Secrecy Scaling
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 33
Network (random extended network):
Nodes are placed in the interval [0, n].
Legitimate nodes randomly placed: Poisson with unit density (n good guys on average)
Eavesdroppers Poisson with le (n) (m(n) = le (n) n bad guys on average.)
n nodes matched into source-destination pairs uniformly at random.
1-D Networks (worst-case topology)
S1
D1
D2
S2
n randomly located nodes -> how much secret information in the presence of m(n) eavesdroppers ?
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 34
A single eavesdropper of known location -> 1-D disconnected (zero secret bits)!
Why? For any node to Eve’s left, Eve is closer (has larger SINR) than the good nodes located to Eve’s right.
What to do? Answer: Nodes help each other to achieve secrecy -> Cooperation.
×
A
E
B
B: Weaker signal
E: Stronger signal
Cooperative Jamming:
E
B
B: Weaker signal, weaker noise
E: Stronger signal, stronger noise
J
A
1-D Networks (worst-case topology)
S
D
Eve
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 35
So, the idea to connect each S-D pair through a sequence of many single-cell hops + one multi-hop jump until reaching D.
Routing Algorithm:
×
×
×
But what if you don’t know where the eavesdroppers are?
Jamming works if you know where the eavesdroppers are.
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 36
×
×
×
Unknown Eavesdropper Locations:
I know how to protect the message if eavesdroppers are spaced far apart.
But this time eavesdroppers can be anywhere.
×
×
×
×
×
×
kth cell
(k+10)th cell
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 37
S
D
x: the b-bit secret message.
S generates t-1 b-bit packets w1, w2, …, wt-1 randomly, sets wt to be such that
x = 1 0 0 1 1
w1 = 0 1 0 1 1
w2 = 1 0 1 1 1
w3 = 0 0 0 1 0
w4 = 0 1 1 0 1
Solution comes with secret sharing at the source
random
random
random
Anyone who has all t packets has the message.
Anyone who misses at least one packet has no information about the message.
For one message, S sends t packets.
The packets are sent in separate transmissions.
Idea: Ensure an eavesdropper anywhere in the network misses at least one packet.
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 38
×
×
×
×
×
×
Divide the network into regions: Coloring the network!
Unknown Eavesdropper Locations:
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 39
Secrecy Analysis:
The only potentially unsecure places: start or the end of a route.
Near-eavesdropper
n/logn eavesdroppers
Standard Scheduling applied: cells take turns in transmissions: throughput per node pair (standard).
Throughput Analysis:
×
×
×
S
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 40
(Insecure) Throughput:
bits per second (per-node throughput) [Gupta-Kumar, 2001]
bits per second (per-node throughput [Franceschetti et al, 2007]
Multi-hop route connecting source-destination pairs.
Two-Dimensional Networks (Review)
If eavesdropper locations are known:
Can route around the “holes” as long as m = o(n/logn) [Koyluoglu et al, 2011]
Also: Securing each hop individually is sufficient to secure the end-to-end route [Koyluoglu et al, 2011]
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 41
Unknown eavesdropper location. What to do?
First answer: Try Cooperative Jamming.
At each hop, some nodes transmit artificial noise to protect the message from eavesdroppers around.
B
J
A
Can tolerate m(n) = log n eavesdroppers
(only). Is this the cost of unknown
eavesdropper positions?
Two-Dimensional Networks
[Vasudevan et al, 2011]
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 42
x = 1 0 0 1 1
w1 = 0 1 0 1 1
w2 = 1 0 1 1 1
w3 = 0 0 0 1 0
w4 = 0 1 1 0 1
Two-Dimensional Networks (Secret Sharing)
random
random
random
An eavesdropper cannot be close to many paths at once…
Except when close to the source or the destination.
Can tolerate n/logn eavesdroppers.
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 43
What about those near eavedroppers?
Problem: near eavesdropper (SNR gap).
We know how to address that: Two-way scheme
(evens out the SNR gap)
Remember, the problem here was:
Near eavesdropper of unknown location.
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 44
The Trick: A Toy Example
An incoming connection can be very useful.
This simple trick has an important implication for wireless secrecy.
Two-way helps address the near eavesdropper problem
1) d generates a random message k and sends it to s.
2) s replies with
(k is used as a one-time pad.)
3) d extracts x from c, k.
e misses k, cannot decode x.
Two nodes + one eavesdropper
e catches whatever s says.
An incoming secure edge is sufficient for secrecy.
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 45
Two-Dimensional Networks
S again generates four packets w1, w2, w3, w4.
But this time, does the two-way scheme with four relays to deliver these packets.
Any Eve here misses k2 -> misses w2
Draining Phase: How we initiate at the source
Routing Algorithm: Draining, routing, delivery
No Eve can be in between for all four r-s pairs.
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 46
Routing Phase:
Delivery Phase:
Carry packets on distant paths.
Come from four directions -> no near eavesdropper can be in between.
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 47
Two-Dimensional Networks
Any Eve here misses k2 -> misses w2
Come from four directions.
No Eve can be in between for all four r-s pairs.
Result: Network can tolerate any
number of eavesdroppers of
arbitrary location at the Gupta-Kumar
per-pair throughput.
Note: Importantly, the same technique can be used in practical networks that are:
sufficiently dense
add infrastructure
IT Security Basics PHY-layer Solutions Using the Network Challenges

## Slide 48
Summary
Information-theoretic security can provide everlasting security – if it can be secured during tranmission.
Exploit the non-commutativity of nonlinear operators to provide a physical-layer approach for disadvantaged environments, but no scheme is completely satisfying.
Perhaps the key is to exploit the network, and two-way communications.
Biggest question: Is information-theoretic security in wireless
just a waste of (mostly academic) resources?
IT Security Basics PHY-layer Solutions Using the Network Challenges